## Slide 1: 3-1 ANALOG AND DIGITAL
Data can be analog or digital.. The term analog data refers to information that is continuous; digital data refers to information that has discrete states. Analog data take on continuous values.. Digital data take on discrete values..
3.1
To be transmitted, data must be transformed to electromagnetic signals
Data can be analog or digital.
Analog data are continuous and take continuous values.
Digital data have discrete states and take discrete values.
Signals can be analog or digital.
Analog signals can have an infinite number of values in a range; digital signals can have only a limited number of values.

## Slide 2: Figure 3.1 Comparison of analog and digital signals
3.2
In data communications, we commonly use periodic analog signals and
nonperiodic digital signals.

## Slide 3: Figure 3.2 A sine wave
3.3

## Slide 4: Example 3.1
The power in your house can be represented by a sine wave with a peak amplitude of 155 to 170 V. However, it is common knowledge that the voltage of th power in
U.S. homes is 110 to 120 V. This discrepancy is due to the fact that these are root mean square (rms) values The signal is squared and then the average amplitude is calculated The peak value is equal to 2½ × rms value

## Slide 5: Figure 3.3 Two signals with the same phase and frequency, but different amplitudes

## Slide 6: Example 3.2
The voltage of a battery is a constant; this constant value can be considered a sine wave, as we will see later. For example, th peak value of an A batter is normally
1.5 V.
Frequency and period are the inverse of
each other.

## Slide 7: Figure 3.4 Two signals with the same amplitude and phase, but different frequencies

## Slide 8: Table 3.1 Units of period and frequency

## Slide 9
Example 3.3
The power we use at home has a frequency of 60 Hz. The period of this sine wave can be determined as follows:

## Slide 10: Example 3.4
Express a period of 100 ms in microseconds.
Solution
From Table 3.1 we find the equivalents of 1 ms (1 ms is 10−3 s) and 1 s (1 s is 106 μs). We make the following substitutions:.

## Slide 11: Example 3.5
The period of a signal is 100 ms. What is its frequency in kilohertz?
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10−3 kHz).

## Slide 12
Frequency is the rate of change with respect to time. Change in a short span of time means high frequency. Change over a long span of time means low frequency.
If a signal does not change at all, its frequency is zero.
If a signal changes instantaneously, its frequency is infinite.
Phase describes the position of the waveform relative to time 0.

## Slide 13: Figure 3.5 Three sine waves with the same amplitude and frequency, but different phases

## Slide 14: Example 3.6
sine wave is offset 1/6 cycle with respect to time 0.
What is its phase in degrees and radians?
Solution
We know that 1 complete cycle is 360°. Therefore, 1/6 cycle is

## Slide 15: Figure 3.6 Wavelength and period

## Slide 16: Figure 3.7 The time-domain and frequency-domain plots of a sine wave

## Slide 17: Note
A complete sine wave in the time domain can be represented by one single spike in the frequency domain.

## Slide 18: Example 3.7
The frequency domain is more compact and useful when we are dealing with more than one sine wave. For example, Figure 3.8 shows three sine waves, each with different amplitude and frequency. All can be represented by three spikes in the frequency domain.

## Slide 19: Figure 3.8 The time domain and frequency domain of three sine waves

## Slide 20
A single-frequency sine wave is not useful in data communications;
we need to send a composite signal, a signal made of many simple sine waves.
According to Fourier analysis, any composite signal is a combination of simple sine waves with different frequencies, amplitudes, and phases.
Fourier analysis is discussed in Appendix C.
If the composite signal is periodic, the decomposition gives a series of signals with discrete frequencies;
if the composite signal is nonperiodic, the decomposition gives a combination of sine waves with continuous frequencies.

## Slide 21: Example 3.8
Figure 3.9 shows a periodic composite signal with frequency f. This type of signal is not typical of those found in data communications We can consider it to be three alarm systems, each with a different frequency. The analysis of this signal can give us a good understanding of how to decompose signals.

## Slide 22: Figure 3.9 A composite periodic signal

## Slide 23: Figure 3.10 Decomposition of a composite periodic signal in the time and frequency domains

## Slide 24: Example 3.9
Figure 3.11 shows a nonperiodic composite signal. It can be the signal created by a microphone or a telephone set when a word or two is pronounced In thi case, the composite signal cannot be periodic, because that implies that we are repeating the same word or words with exactly the same tone.

## Slide 25: Figure 3.11 The time and frequency domains of a nonperiodic signal

## Slide 26: Note
The bandwidth of a composite signal is the difference between the
highest and the lowest frequencies contained in that signal.

## Slide 27: Figure 3.12 The bandwidth of periodic and nonperiodic composite signals

## Slide 28: Example 3.10
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V. Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
The spectrum has only five spikes, at 100, 300, 500, 700,
and 900 Hz (see Figure 3.13).

## Slide 29: Figure 3.13 The bandwidth for Example 3.10

## Slide 30: Example 3.11
A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all frequencies of the same amplitude.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
The spectrum contains all integer frequencies. We show this by a series of spikes (see Figure 3.14).

## Slide 31: Figure 3.14 The bandwidth for Example 3.11

## Slide 32: Example 3.12
nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz Figure 3 15 shows the frequency domain and the bandwidth.

## Slide 33: Figure 3.15 The bandwidth for Example 3.12

## Slide 34: Example 3.13
An example of a nonperiodic composite signal is the signal propagated by an AM radio station. In the United States, each AM radio station is assigned a 10-kHz bandwidth. The total bandwidth dedicated to AM radio ranges from 530 to 1700 kHz. We will show the rationale behind this 10-kHz bandwidth in Chapter 5.

## Slide 35: Example 3.14
Another example of a nonperiodic composite signal is the signal propagated by an FM radio station. In the United States, each FM radio station is assigned a 200- kHz bandwidth. The total bandwidth dedicated to FM radio ranges from 88 to 108 MHz We will show the rationale behind this 200-kHz bandwidth in Chapter 5.

## Slide 36: Example 3.15
Another example of a nonperiodic composite signal is the signal received by an old-fashioned analog black- and-white TV. A TV screen is made up of pixels. If we assume a resolution of 525 × 700, we have 367,500 pixels per screen. If we scan the screen 30 times per second, this is 367,500 × 30 = 11,025,000 pixels per second. The worst-case scenario is alternating black and white pixels. We can send 2 pixels per cycle. Therefore, we need 11,025,000 / 2 = 5,512,500 cycles per second, or Hz. The bandwidth needed is 5.5125 MHz.

## Slide 37: 3-3 DIGITAL SIGNALS
In addition to being represented by an analog signal, information can also be represented by a digital signal.... For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage.... A digital signal can have more than two levels. In this case, we can send more than 1 bit for each level....
Topics discussed in this section:
Bit Rate Bit Length
Digital Signal as a Composite Analog Signal Application Layer

## Slide 38: Figure 3.16 Two digital signals: one with two signal levels and the other with four signal levels

## Slide 39: Example 3.16
digital signal has eight levels. How many bits are needed per level? We calculate the number of bits from the formula
Each signal level is represented by 3 bits.

## Slide 40: Example 3.17
digital signal has nine levels. How many bits are needed per level? We calculate the number of bits by using the formula Each signal level is represented by
3.17 bits. However, this answer is not realistic. The number of bits sent per level needs to be an integer as well as a power of 2. For this example, 4 bits can represent one level

## Slide 41: Example 3.18
Assume we need to download text documents at the rate of 100 pages per second. What is the required bit rate of the channel?
Solution
page is an average of 24 lines with 80 characters in each line. If we assume that one character requires 8 bits, the bit rate is

## Slide 42: Example 3.19
A digitized voice channel, as we will see in Chapter 4, is made by digitizing a 4-kHz bandwidth analog voice signal. We need to sample the signal at twice the highest frequency (two samples per hertz). We assume that each sample requires 8 bits. What is the required bit rate?
Solution
The bit rate can be calculated as

## Slide 43: Example 3.20
What is the bit rate for high-definition TV (HDTV)?
Solution
HDTV uses digital signals to broadcast high quality video signals. The HDTV screen is normally a ratio of 16 : 9. There are 1920 by 1080 pixels per screen, and the screen is renewed 30 times per second. Twenty-four bits represents one color pixel.
The TV stations reduce this rate to 20 to 40 Mbps through compression.

## Slide 44: Figure 3.17 The time and frequency domains of periodic and nonperiodic digital signals

## Slide 45: Figure 3.18 Baseband transmission
A digital signal is a composite analog
signal with an infinite bandwidth.

## Slide 46: Figure 3.19 Bandwidths of two low-pass channels

## Slide 47: Figure 3.20 Baseband transmission using a dedicated medium

## Slide 48: Note
very wide bandwidth.
Baseband transmission of a digital signal that preserves the shape of the digital signal is possible only if we have a low-pass channel with an infinite or

## Slide 49: Example 3.21
An example of a dedicated channel where the entire bandwidth of the medium is used as one single channel is a LAN. Almost every wired LAN today uses a dedicated channel for two stations communicating with each other. In a bus topology LAN with multipoint connections, only two stations can communicate with each other at each moment in time (timesharing); the other stations need to refrain from sending data. In a star topology LAN, the entire channel between each station and the hub is used for communication between these two entities. We study LANs in Chapter 14.

## Slide 50: Figure 3.21 Rough approximation of a digital signal using the first harmonic for worst case

## Slide 51: Figure 3.22 Simulating a digital signal with first three harmonics

## Slide 52
In baseband transmission, the required bandwidth is
proportional to the bit rate;
if we need to send bits faster, we need more bandwidth.
if we need to send bits faster, we need
more bandwidth.

## Slide 53: Table 3.2 Bandwidth requirements

## Slide 54: Example 3.22
What is the required bandwidth of a low-pass channel if we need to send 1 Mbps by using baseband transmission?
Solution
The answer depends on the accuracy desired.
The minimum bandwidth, is B = bit rate /2, or 500 kHz.
A better solution is to use the first and the third harmonics with B = 3 × 500 kHz = 1.5 MHz.
Still a better solution is to use the first, third, and fifth harmonics with B = 5 × 500 kHz = 2.5 MHz.

## Slide 55: Example 3.22
We have a low-pass channel with bandwidth 100 kHz.
What is the maximum bit rate of this
channel?
Solution
The maximum bit rate can be achieved if we use the first harmonic. The bit rate is 2 times the available bandwidth, or 200 kbps.

## Slide 56: Figure 3.23 Bandwidth of a bandpass channel

## Slide 57: Note
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel;
we need to convert the digital signal to an analog signal before transmission.

## Slide 58: Figure 3.24 Modulation of a digital signal for transmission on a bandpass channel

## Slide 59: Example 3.24
An example of broadband transmission using modulation is the sending of computer data through a telephone subscriber line, the line connecting a resident to the central telephone office. These lines are designed to carry voice with a limited bandwidth. The channel is considered a bandpass channel. We convert the digital signal from the computer to an analog signal, and send the analog signal. We can install two converters to change the digital signal to analog and vice versa at the receiving end. The converter, in this case, is called a modem which we discuss in detail in Chapter 5.

## Slide 60: Example 3.25
second example is the digital cellular telephone. For better reception, digital cellular phones convert the analog voice signal to a digital signal (see Chapter 16) Although the bandwidth allocated to a company providing digital cellular phone service is very wide, we still cannot send the digital signal without conversion. The reason is that we only have a bandpass channel available between caller and callee. We need to convert the digitized voice to a composite analog signal before sending.

## Slide 61: 3-4 TRANSMISSION IMPAIRMENT
Signals travel through transmission media, which are not perfect.. The imperfection causes signal impairment.. This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium.. What is sent is not what is received. Three causes of impairment are attenuation,, distortion,, and noise..
Topics discussed in this section:
Attenuation Distortion Noise

## Slide 62: Figure 3.25 Causes of impairment

## Slide 63: Figure 3.26 Attenuation

## Slide 64: Figure 3.27 Decibels for Example 3.28

## Slide 65: Figure 3.28 Distortion

## Slide 66: Figure 3.29 Noise

## Slide 67: Figure 3.30 Two cases of SNR: a high SNR and a low SNR

## Slide 68: 3-5 DATA RATE LIMITS
A very important consideration in data communications is how fast we can send data, in bits per second, over a channel. Data rate depends on three factors:
1.. The bandwidth available
2. The level of the signals we use
3.. The quality of the channel (the level of noise)
Increasing the levels of a signal may reduce the reliability of the system.

## Slide 69: Example 3.33
Does the Nyquist theorem bit rate agree with the intuitive bit rate described in baseband transmission?
Solution
They match when we have only two levels We said, in baseband transmission, the bit rate is 2 times the bandwidth if we use only the first harmonic in the worst case. However, the Nyquist formula is more general than what we derived intuitively; it can be applied to baseband transmission and modulation. Also, it can be applied when we have two or more levels of signals

## Slide 70: Figure 3.31 Filling the link with bits for case 1
3.70

## Slide 71: Example 3.48
We can think about the link between two points as a pipe. The cross section of the pipe represents the bandwidth, and the length of th pipe represents th delay. We can say the volume of the pipe defines the bandwidth-delay product, as shown in Figure 3 33
3.71

## Slide 72: Figure 3.32 Filling the link with bits in case 2
3.72

## Slide 73: Figure 3.33 Concept of bandwidth-delay product
3.73
The bandwidth-delay product defines the number of bits that can fill the link

## Slide 74: 4-1 DIGITAL-TO-DIGITAL CONVERSION
In this section, we see how we can represent digital data by using digital signals. The conversion involves
three techniques: line coding,, block coding,,
scrambling.. Line coding is always needed;
and block
coding and scrambling may or may not be needed..
Topics discussed in this section:
Line Coding
Line Coding Schemes Block Coding Scrambling
4.2

## Slide 75: Figure 4.1 Line coding and decoding
4.3

## Slide 76: Figure 4.2 Signal element versus data element
4.4

## Slide 77: Note
Although the actual bandwidth of a digital signal is infinite, the effective bandwidth is finite.
4.6

## Slide 78: Figure 4.3 Effect of lack of synchronization
4.8

## Slide 79: Example 4.3
In a digital transmission, the receiver clock is 0.1 percent faster than the sender clock. How many extra bits per second does the receiver receive if the data rate is 1 kbps? How many if the data rate is 1 Mbps?
Solution
At 1 kbps, the receiver receives 1001 bps instead of 1000 bps.
At 1 Mbps, the receiver receives 1,001,000 bps instead of 1,000,000 bps.
4.9

## Slide 80: Figure 4.4 Line coding schemes

## Slide 81: Figure 4.5 Unipolar NRZ scheme

## Slide 82: Figure 4.6 Polar NRZ-L and NRZ-I schemes

## Slide 83
In NRZ-L the level of the voltage determines the value of the bit.
In NRZ-I the inversion or the lack of inversion
determines the value of the bit.
NRZ-L and NRZ-I both have an average signal rate of N/2 Bd.
NRZ-L and NRZ-I both have a DC component problem.

## Slide 84: Example 4.4
A system is using NRZ-I to transfer 1-Mbps data. What are the average signal rate and minimum bandwidth?
Solution
The average signal rate is S = N/2 = 500 kbaud. The minimum bandwidth for this average baud rate is Bmin = S = 500 kHz.

## Slide 85: Figure 4.7 Polar RZ scheme

## Slide 86: Figure 4.8 Polar biphase: Manchester and differential Manchester schemes

## Slide 87
In Manchester and differential Manchester encoding, the transition at the middle of the bit is used for synchronization.
The minimum bandwidth of Manchester and differential Manchester is 2 times that of NRZ.
In bipolar encoding, we use three levels: positive, zero, and negative.

## Slide 88: Figure 4.9 Bipolar schemes: AMI and pseudoternary

## Slide 89: Note
In mBnL schemes, a pattern of m data elements is encoded as a pattern of n signal elements in which 2m ≤ Ln.

## Slide 90: Figure 4.10 Multilevel: 2B1Q scheme

## Slide 91: Figure 4.11 Multilevel: 8B6T scheme

## Slide 92: Figure 4.12 Multilevel: 4D-PAM5 scheme

## Slide 93: Figure 4.13 Multitransition: MLT-3 scheme

## Slide 94: Table 4.1 Summary of line coding schemes

## Slide 95: Note
Block coding is normally referred to as
mB/nB coding;
it replaces each m-bit group with an
n-bit group.

## Slide 96: Figure 4.14 Block coding concept

## Slide 97: Figure 4.15 Using block coding 4B/5B with NRZ-I line coding scheme

## Slide 98: Table 4.2 4B/5B mapping codes

## Slide 99: Figure 4.16 Substitution in 4B/5B block coding

## Slide 100: Example 4.5
We need to send data at a 1-Mbps rate. What is the minimum required bandwidth, using a combination of 4B/5B and NRZ-I or Manchester coding?
Solution
First 4B/5B block coding increases the bit rate to 1.25 Mbps. The minimum bandwidth using NRZ-I is N/2 or 625 kHz. The Manchester scheme needs a minimum bandwidth of 1 MHz. The first choice needs a lower bandwidth, but has a DC component problem; the second choice needs a higher bandwidth, but does not have a DC component problem

## Slide 101: Figure 4.17 8B/10B block encoding

## Slide 102: Figure 4.18 AMI used with scrambling

## Slide 103: Figure 4.19 Two cases of B8ZS scrambling technique

## Slide 104: Note
B8ZS substitutes eight consecutive zeros with 000VB0VB.

## Slide 105: Figure 4.20 Different situations in HDB3 scrambling technique

## Slide 106: Note
HDB3 substitutes four consecutive zeros with 000V or B00V depending on the number of nonzero pulses after the last substitution.

## Slide 107: 4-2 ANALOG-TO-DIGITAL CONVERSION
We have seen in Chapter 3 that a digital signal is superior to an analog signal. The tendency today is to change an analog signal to digital data.. In this section we describe two techniques, pulse code modulation and delta modulation..
Topics discussed in this section: Pulse Code Modulation (PCM) Delta Modulation (DM)

## Slide 108: Figure 4.21 Components of PCM encoder

## Slide 109: Figure 4.22 Three different sampling methods for PCM

## Slide 110: Note
According to the Nyquist theorem, the sampling rate must be
at least 2 times the highest frequency contained in the signal.

## Slide 111: Figure 4.23 Nyquist sampling rate for low-pass and bandpass signals

## Slide 112: Example 4.6
For an intuitive example of the Nyquist theorem, let us sample a simple sine wave at three sampling rates: fs = 4f (2 times the Nyquist rate), fs = 2f (Nyquist rate), and fs = f (one-half the Nyquist rate). Figure 4.24 shows the sampling and the subsequent recovery of the signal.
It can be seen that sampling at the Nyquist rate can create a good approximation of the original sine wave (part a).
Oversampling in part
approximation, but it
b can also create the same is redundant and unnecessary.
Sampling below the Nyquist rate (part c) does not produce a signal that looks like the original sine wave.

## Slide 113: Figure 4.24 Recovery of a sampled sine wave for different sampling rates

## Slide 114: Example 4.7
Consider the revolution of a hand of a clock. The second hand of a clock has a period of 60 s. According to the Nyquist theorem, we need to sample the hand every 30 s (Ts = T or fs = 2f ). In Figure 4.25a, the sample points, in order, are 12, 6, 12, 6, 12, and 6. The receiver of the samples cannot tell if the clock is moving forward or backward. In part b, we sample at double the Nyquist rate (every 15 s). The sample points are 12, 3, 6, 9, and 12. The clock is moving forward. In part c, we sample below the Nyquist rate (Ts = T or fs = f ). The sample points are 12, 9, 6, 3, and 12. Although the clock is moving forward, the receiver thinks that the clock is moving backward.

## Slide 115: Figure 4.25 Sampling of a clock with only one hand

## Slide 116: Example 4.8
An example related to Example 4.7 is the seemingly backward rotation of the wheels of a forward-moving car in a movie. This can be explained by under-sampling. A movie is filmed at 24 frames per second. If a wheel is rotating more than 12 times per second, the under- sampling creates the impression of a backward rotation.
Telephone companies digitize voice by assuming a maximum frequency of 4000 Hz. The sampling rate therefore is 8000 samples per second.

## Slide 117: Example 4.10
A complex low-pass signal has a bandwidth of 200 kHz. What is the minimum sampling rate for this signal?
Solution
The bandwidth of a low-pass signal is between 0 and f, where f is the maximum frequency in the signal Therefore, we can sample this signal at 2 times the highest frequency (200 kHz) The sampling rate is therefore 400,000 samples per second.

## Slide 118: Example 4.11
A complex bandpass signal has a bandwidth of 200 kHz. What is the minimum sampling rate for this signal?
Solution
We cannot find the minimum sampling rate in this case because we do not know where the bandwidth starts or ends. We do not know the maximum frequency in the signal

## Slide 119: Figure 4.26 Quantization and encoding of a sampled signal

## Slide 120: Example 4.12
What is the SNRdB in the example of Figure 4.26?
Solution
We can use the formula to find the quantization. We have eight levels and 3 bits per sample, so
SNRdB = 6 02(3) + 1 76 = 19 82 dB
Increasing the number of levels increases the SNR.

## Slide 121: Example 4.13
A telephone subscriber line must have an SNRdB above
40. What is the minimum number of bits per sample?
Solution
We can calculate the number of bits as
Telephone companies usually assign 7 or 8 bits per sample.

## Slide 122: Example 4.14
We want to digitize the human voice. What is the bit rate, assuming 8 bits per sample?
Solution
The human voice normally contains frequencies from 0 to 4000 Hz. So the sampling rate and bit rate are calculated as follows:

## Slide 123: Figure 4.27 Components of a PCM decoder

## Slide 124: Example 4.15
We have a low-pass analog signal of 4 kHz. If we send the analog signal, we need a channel with a minimum bandwidth of 4 kHz. If we digitize the signal and send 8 bits per sample, we need a channel with a minimum bandwidth of 8 × 4 kHz = 32 kHz.

## Slide 125: Figure 4.28 The process of delta modulation

## Slide 126: Figure 4.29 Delta modulation components

## Slide 127: Figure 4.30 Delta demodulation components

## Slide 128: 4-3 TRANSMISSION MODES
The transmission of binary data across a link can be accomplished in either parallel or serial mode. In parallel mode, multiple bits are sent with each clock tick. In serial mode, 1 bit is sent with each clock tick. While there is only one way to send parallel data, there are three subclasses of serial transmission: asynchronous, synchronous, and isochronous..
Topics discussed in this section:
Parallel Transmission Serial Transmission

## Slide 129: Figure 4.31 Data transmission and modes

## Slide 130: Figure 4.32 Parallel transmission

## Slide 131: Figure 4.33 Serial transmission

## Slide 132
In asynchronous transmission, we send 1 start bit (0) at the beginning and 1 or more stop bits (1s) at the end of each byte. There may be a gap between
each byte.
Asynchronous here means “asynchronous at the byte level,” but the bits are still synchronized; their durations are the same.

## Slide 133: Figure 4.34 Asynchronous transmission
In synchronous transmission, we send bits one after another without start or stop bits or gaps. It is the responsibility of the receiver to group the bits.

## Slide 134: Figure 4.35 Synchronous transmission

## Slide 135: 5-1 DIGITAL-TO-ANALOG CONVERSION
Digital-to-analog conversion is the process of changing one of the characteristics of an analog signal based on the information in digital data..
Topics discussed in this section: Aspects of Digital-to-Analog Conversion Amplitude Shift Keying
Frequency Shift Keying Phase Shift Keying
Quadrature Amplitude Modulation
5.2

## Slide 136: Figure 5.1 Digital-to-analog conversion
5.3

## Slide 137: Figure 5.2 Types of digital-to-analog conversion
5.4

## Slide 138: Note
Bit rate is the number of bits per second.
Baud rate is the number of signal elements per second.
In the analog transmission of digital data, the baud rate is less than
or equal to the bit rate.
5.5

## Slide 139: Example 5.1
An analog signal carries 4 bits per signal element. If 1000 signal elements are sent per second, find the bit rate.
Solution
In this case, r = 4, S = 1000, and N is unknown. We can find the value of N from
5.6

## Slide 140: Example 5.2
An analog signal has a bit rate of 8000 bps and a baud rate of 1000 baud. How many data elements are carried by each signal element? How many signal elements do we need?
Solution
In this example, S = 1000, N = 8000, and r and L are unknown. We find first the value of r and then the value of L.
5.7

## Slide 141: Figure 5.3 Binary amplitude shift keying
5.8

## Slide 142: Figure 5.4 Implementation of binary ASK
5.9

## Slide 143: Example 5.3
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What are the carrier frequency and the bit rate if we modulated our data by using ASK with d = 1?
Solution
The middle of the bandwidth is located at 250 kHz. This means that our carrier frequency can be at fc = 250 kHz. We can use the formula for bandwidth to find the bit rate (with d = 1 and r = 1).
5.10

## Slide 144: Example 5.4
In data communications, we normally use full-duplex links with communication in both directions. We need to divide th bandwidth into two with two carrier frequencies, as shown in Figure 5.5. The figure shows
the positions of two carrier frequencies
and the bandwidths. The available bandwidth for each
direction is now 50 kHz, which leaves us with a data rate of 25 kbps in each direction.
5.11

## Slide 145: Figure 5.5 Bandwidth of full-duplex ASK used in Example 5.4
5.12

## Slide 146: Figure 5.6 Binary frequency shift keying
5.13

## Slide 147: Example 5.5
We have an available bandwidth of 100 kHz which spans from 200 to 300 kHz. What should be the carrier frequency and the bit rate if we modulated our data by using FSK with d = 1?
Solution
This problem is similar to Example 5.3, but we are modulating by using FSK. The midpoint of the band is at 250 kHz. We choose 2Δf to be 50 kHz; this means
5.14

## Slide 148: Figure 5.7 Bandwidth of MFSK used in Example 5.6
5.15

## Slide 149: Example 5.6
We need to send data 3 bits at a time at a bit rate of 3 Mbps. The carrier frequency is 10 MHz. Calculate the number of levels (different frequencies), the baud rate, and the bandwidth.
Solution
We can have L = 23 = 8. The baud rate is S = 3 MHz/3 = 1000 Mbaud. This means that the carrier frequencies must be 1 MHz apart (2Δf = 1 MHz). The bandwidth is B
= 8 × 1000 = 8000. Figure 5.8 shows the allocation of frequencies and bandwidth.
5.16

## Slide 150: Figure 5.8 Bandwidth of MFSK used in Example 5.6
5.17

## Slide 151: Figure 5.9 Binary phase shift keying
5.18

## Slide 152: Figure 5.10 Implementation of BASK
5.19

## Slide 153: Figure 5.11 QPSK and its implementation
5.20

## Slide 154: Example 5.7
Find the bandwidth for a signal transmitting at 12 Mbps for QPSK. The value of d = 0.
5.21
Solution
For QPSK, 2 bits is carried by one signal element. This means that r = 2. So the signal rate (baud rate) is S = N × (1/r) = 6 Mbaud. With a value of d = 0, we have B = S = 6 MHz.

## Slide 155: Figure 5.12 Concept of a constellation diagram
5.22

## Slide 156: Example 5.8
Show the constellation diagrams for an ASK (OOK), BPSK, and QPSK signals.
Solution
Figure 5.13 shows the three constellation diagrams.
5.23

## Slide 157: Figure 5.13 Three constellation diagrams
5.24

## Slide 158: Note
Quadrature amplitude modulation is a
combination of ASK and PSK.
5.25

## Slide 159: Figure 5.14 Constellation diagrams for some QAMs
5.26

## Slide 160: 5-2 ANALOG AND DIGITAL
Analog-to-analog conversion is the representation of analog information by an analog signal. One may ask why we need to modulate an analog signal; it is already analog. Modulation is needed if the medium is bandpass in nature or if only a bandpass channel is available to us.
Topics discussed in this section:
Amplitude Modulation Frequency Modulation Phase Modulation
5.27

## Slide 161: Figure 5.15 Types of analog-to-analog modulation
5.28

## Slide 162: Figure 5.16 Amplitude modulation
5.29

## Slide 163: Note
The total bandwidth required for AM can be determined
from the bandwidth of the audio signal: BAM = 2B.
5.30

## Slide 164: Figure 5.17 AM band allocation
5.31

## Slide 165: Note
The total bandwidth required for FM can be determined from the bandwidth
of the audio signal: BFM = 2(1 + β)B.
5.32

## Slide 166: Figure 5.18 Frequency modulation
5.33

## Slide 167: Figure 5.19 FM band allocation
5.34

## Slide 168: Figure 5.20 Phase modulation
5.35

## Slide 169: Note
The total bandwidth required for PM can be determined from the bandwidth
and maximum amplitude of the modulating signal:
BPM = 2(1 + β)B.
5.36

## Slide 170: Note
Bandwidth utilization is the wise use of available bandwidth to achieve specific goals.
Efficiency can be achieved by multiplexing; privacy and anti-jamming can be achieved by spreading.
6.2

## Slide 171: 6-1 MULTIPLEXING
Whenever the bandwidth of a medium linking two devices is greater than the bandwidth needs of the devices, the link can be shared. Multiplexing is the set of techniques that allows the simultaneous transmission of multiple signals across a single data link.. As data and telecommunications use increases, so does traffic.
Topics discussed in this section: Frequency-Division Multiplexing Wavelength-Division Multiplexing Synchronous Time-Division Multiplexing Statistical Time-Division Multiplexing
6.3

## Slide 172: Figure 6.1 Dividing a link into channels
6.4

## Slide 173: Figure 6.2 Categories of multiplexing
6.5

## Slide 174: Figure 6.3 Frequency-division multiplexing
6.6
FDM is an analog multiplexing technique that combines analog signals.

## Slide 175: Figure 6.4 FDM process
6.8

## Slide 176: Figure 6.5 FDM demultiplexing example
6.9

## Slide 177: Example 6.1
Assume that a voice channel occupies a bandwidth of 4 kHz. We need to combine three voice channels into a link with a bandwidth of 12 kHz, from 20 to 32 kHz. Show the configuration, using the frequency domain. Assume there are no guard bands.
Solution
We shift (modulate) each of the three voice channels to a different bandwidth, as shown in Figure 6.6. We use the 20- to 24-kHz bandwidth for the first channel, the 24- to 28-kHz bandwidth for the second channel, and the 28- to 32-kHz bandwidth for the third one. Then we combine them as shown in Figure 6.6.

## Slide 178: Figure 6.6 Example 6.1

## Slide 179: Example 6.2
Five channels, each with a 100-kHz bandwidth, are to be multiplexed together. What is the minimum bandwidth of th link if ther is a need for a guard band of 10 kHz between the channels to prevent interference?
Solution
For five channels, we need at least four guard bands. This means that the required bandwidth is at least
5 × 100 + 4 × 10 = 540 kHz,
as shown in Figure 6.7.

## Slide 180: Figure 6.7 Example 6.2

## Slide 181: Example 6.3
Four data channels (digital), each transmitting at 1 Mbps, use a satellite channel of 1 MHz. Design an appropriate configuration, using FDM
Solution
The satellite channel is analog. We divide it into four channels, each channel having a 250-kHz bandwidth. Each digital channel of 1 Mbps is modulated such that each 4 bits is modulated to 1 Hz. One solution is 16-QAM modulation. Figure 6.8 shows one possible configuration.

## Slide 182: Figure 6.8 Example 6.3

## Slide 183: Figure 6.9 Analog hierarchy

## Slide 184: Example 6.4
The Advanced Mobile Phone System (AMPS) uses two bands The first band of 824 to 849 MHz is used for sending, and 869 to 894 MHz is used for receiving. Each user has a bandwidth of 30 kHz in each direction
How many people can use their cellular phones
simultaneously? Solution
Each band is 25 MHz. If we divide 25 MHz by 30 kHz, we
get 833.33. In reality, the band is divided into 832 channels. Of these, 42 channels are used for control, which means only 790 channels are available for cellular phone users.

## Slide 185: Figure 6.10 Wavelength-division multiplexing

## Slide 186
Note
WDM is an analog multiplexing technique to combine optical signals.

## Slide 187: Figure 6.11 Prisms in wavelength-division multiplexing and demultiplexing

## Slide 188: Figure 6.12 TDM
TDM is a digital multiplexing technique for combining several low-rate channels into one high-rate one.

## Slide 189: Figure 6.13 Synchronous time-division multiplexing

## Slide 190: Note
In synchronous TDM, the data rate of the link is n times faster, and the unit
duration is n times shorter.

## Slide 191: Example 6.5
In Figure 6.13, the data rate for each input connection is 3 kbps. If 1 bit at a time is multiplexed (a unit is 1 bit), what is the duration of (a) each input slot, (b) each output slot, and (c) each frame?
Solution
We can answer the questions as follows:
a. The data rate of each input connection is 1 kbps. This means that the bit duration is 1/1000 s or 1 ms. The duration of the input time slot is 1 ms (same as bit duration).

## Slide 192: Example 6.5 (continued)
b. The duration of each output time slot is one-third of the input time slot. This means that the duration of the output time slot is 1/3 ms.
c. Each frame carries three output time slots. So the duration of a frame is 3 × 1/3 ms, or 1 ms. The duration of a frame is the same as the duration of an input unit.

## Slide 193: Example 6.6
Figure 6.14 shows synchronous TDM with a data stream for each input and one data stream for the output. The unit of data is 1 bit. Find (a) the input bit duration, (b) the output bit duration, (c) the output bit rate, and (d) the output frame rate.
Solution
We can answer the questions as follows:
The input bit duration is the inverse of the bit rate: 1/1 Mbps = 1 μs.
The output bit duration is one-fourth of the input bit duration, or ¼ μs.

## Slide 194: Example 6.6 (continued)
c. The output bit rate is the inverse of the output bit duration or 1/(4μs) or 4 Mbps. This can also be deduced from the fact that the output rate is 4 times as fast as any input rate; so the output rate = 4 × 1 Mbps
= 4 Mbps.
d. The frame rate is always the same as any input rate. So the frame rate is 1,000,000 frames per second. Because we are sending 4 bits in each frame, we can verify the result of the previous question by multiplying the frame rate by the number of bits per frame.

## Slide 195: Figure 6.14 Example 6.6

## Slide 196: Example 6.7
Four 1-kbps connections are multiplexed together. A unit is 1 bit. Find (a) the duration of 1 bit before multiplexing,
(b) the transmission rate of the link, (c) the duration of a time slot, and (d) the duration of a frame.
Solution
We can answer the questions as follows:
The duration of 1 bit before multiplexing is 1 / 1 kbps, or 0.001 s (1 ms).
The rate of the link is 4 times the rate of a connection, or 4 kbps.

## Slide 197: Example 6.7 (continued)
c. The duration of each time slot is one-fourth of the duration of each bit before multiplexing, or 1/4 ms or 250 μs. Note that we can also calculate this from the data rate of the link, 4 kbps. The bit duration is the inverse of the data rate, or 1/4 kbps or 250 μs.
d. The duration of a frame is always the same as the duration of a unit before multiplexing, or 1 ms. We can also calculate this in another way. Each frame in this case has four time slots. So the duration of a frame is 4 times 250 μs, or 1 ms.

## Slide 198: Figure 6.15 Interleaving

## Slide 199: Example 6.8
Four channels are multiplexed using TDM. If each channel sends 100 bytes /s and we multiplex 1 byte per channel, show the frame traveling on the link, the size of the frame, the duration of a frame, the frame rate, and the bit rate for the link.
Solution
The multiplexer is shown in Figure 6.16. Each frame carries 1 byte from each channel; the size of each frame, therefore, is 4 bytes, or 32 bits. Because each channel is sending 100 bytes/s and a frame carries 1 byte from each channel, the frame rate must be 100 frames per second. The bit rate is 100 × 32, or 3200 bps.

## Slide 200: Figure 6.16 Example 6.8

## Slide 201: Example 6.9
A multiplexer combines four 100-kbps channels using a time slot of 2 bits. Show the output with four arbitrary inputs. What is the frame rate? What is the frame duration? What is the bit rate? What is the bit duration?
Solution
Figure 6.17 shows the output for four arbitrary inputs. The link carries 50,000 frames per second. The frame duration is therefore 1/50,000 s or 20 μs. The frame rate is 50,000 frames per second, and each frame carries 8 bits; the bit rate is 50,000 × 8 = 400,000 bits or 400 kbps. The bit duration is 1/400,000 s, or 2.5 μs.

## Slide 202: Figure 6.17 Example 6.9

## Slide 203: Figure 6.18 Empty slots

## Slide 204: Figure 6.19 Multilevel multiplexing

## Slide 205: Figure 6.20 Multiple-slot multiplexing

## Slide 206: Figure 6.21 Pulse stuffing

## Slide 207: Figure 6.22 Framing bits

## Slide 208: Example 6.10
We have four sources, each creating 250 characters per second. If the interleaved unit is a character and 1 synchronizing bit is added to each frame, find (a) the data rate of each source, (b) the duration of each character in each source, (c) the frame rate, (d) the duration of each frame, (e) the number of bits in each frame, and (f) the data rate of the link.
Solution
We can answer the questions as follows:
a. The data rate of each source is 250 × 8 = 2000 bps = 2 kbps.

## Slide 209: Example 6.10 (continued)
Each source sends 250 characters per second; therefore, the duration of a character is 1/250 s, or 4 ms.
Each frame has one character from each source, which means the link needs to send 250 frames per second to keep the transmission rate of each source.
The duration of each frame is 1/250 s, or 4 ms. Note that the duration of each frame is the same as the duration of each character coming from each source.
Each frame carries 4 characters and 1 extra synchronizing bit. This means that each frame is 4 × 8 + 1 = 33 bits.

## Slide 210: Example 6.11
Two channels, one with a bit rate of 100 kbps and another with a bit rate of 200 kbps, are to be multiplexed How this can be achieved? What is the frame rate? What is the frame duration? What is the bit rate of the link?
Solution
We can allocate one slot to the first channel and two slots to the second channel. Each frame carries 3 bits. The frame rate is 100,000 frames per second because it carries
1 bit from the first channel. The bit rate is 100,000 frames/s × 3 bits per frame, or 300 kbps.

## Slide 211: Figure 6.23 Digital hierarchy

## Slide 212: Table 6.1 DS and T line rates

## Slide 213: Figure 6.24 T-1 line for multiplexing telephone lines

## Slide 214: Figure 6.25 T-1 frame structure

## Slide 215: Table 6.2 E line rates

## Slide 216: Figure 6.26 TDM slot comparison

## Slide 217: Figure 7.1 Transmission medium and physical layer
7.2

## Slide 218: Figure 7.2 Classes of transmission media
7.3

## Slide 219: 7-1 GUIDED MEDIA
Guided media, which are those that provide a conduit from one device to another, include twisted-pair cable, coaxial cable, and fiber-optic cable..
7.4
Topics discussed in this section:
Twisted-Pair Cable Coaxial Cable Fiber-Optic Cable

## Slide 220: Figure 7.3 Twisted-pair cable
7.5

## Slide 221: Figure 7.4 UTP and STP cables
7.6

## Slide 222: Table 7.1 Categories of unshielded twisted-pair cables
7.7

## Slide 223: Figure 7.5 UTP connector
7.8

## Slide 224: Figure 7.6 UTP performance
7.9

## Slide 225: Figure 7.7 Coaxial cable

## Slide 226: Table 7.2 Categories of coaxial cables

## Slide 227: Figure 7.8 BNC connectors

## Slide 228: Figure 7.9 Coaxial cable performance

## Slide 229: Figure 7.10 Bending of light ray

## Slide 230: Figure 7.11 Optical fiber

## Slide 231: Figure 7.12 Propagation modes

## Slide 232: Figure 7.13 Modes

## Slide 233: Table 7.3 Fiber types

## Slide 234: Figure 7.14 Fiber construction

## Slide 235: Figure 7.15 Fiber-optic cable connectors

## Slide 236: Figure 7.16 Optical fiber performance

## Slide 237: 7-2 UNGUIDED MEDIA: WIRELESS
Unguided media transport electromagnetic
waves without using a physical conductor. This type of
communication is often referred to as wireless communication.
Topics discussed in this section:
Radio Waves Microwaves Infrared

## Slide 238: Figure 7.17 Electromagnetic spectrum for wireless communication

## Slide 239: Figure 7.18 Propagation methods

## Slide 240: Table 7.4 Bands

## Slide 241: Figure 7.19 Wireless transmission waves

## Slide 242: Figure 7.20 Omnidirectional antenna

## Slide 243: Note
Radio waves are used for multicast communications, such as radio and television, and paging systems.

## Slide 244: Figure 7.21 Unidirectional antennas

## Slide 245
Microwaves are used for unicast communication such as cellular telephones, satellite networks, and wireless LANs.
Infrared signals can be used for short- range communication in a closed area using line-of-sight propagation.

## Slide 246: Figure 8.1 Switched network
8.2

## Slide 247: Figure 8.2 Taxonomy of switched networks
8.3

## Slide 248: 8-1 CIRCUIT-SWITCHED NETWORKS
A circuit-switched network consists of a set of switches connected by physical links. A connection between two stations is a dedicated path made of one or more links.. However, each connection uses only one dedicated channel on each link.. Each link is normally divided into n channels by using FDM or TDM.
Topics discussed in this section:
Three Phases Efficiency Delay
Circuit-Switched Technology in Telephone Networks
8.4

## Slide 249: Note
A circuit-switched network is made of a set of switches connected by physical links, in which each link is
divided into n channels.
8.5

## Slide 250: Figure 8.3 A trivial circuit-switched network
8.6

## Slide 251: Note
In circuit switching, the resources need to be reserved during the setup phase; the resources remain dedicated for the entire duration of data transfer until the teardown phase.
8.7

## Slide 252: Example 8.1
As a trivial example, let us use a circuit-switched network to connect eight telephones in a small area. Communication is through 4-kHz voice channels. We assume that each link uses FDM to connect a maximum of two voice channels. The bandwidth of each link is then 8 kHz. Figure 8.4 shows the situation. Telephone 1 is connected to telephone 7; 2 to 5; 3 to 8; and 4 to 6. Of course the situation may change when new connections are made. The switch controls the connections.
8.8

## Slide 253: Figure 8.4 Circuit-switched network used in Example 8.1
8.9

## Slide 254: Example 8.2
As another example, consider a circuit-switched network that connects computers in two remote offices of a private company. The offices are connected using a T-1 line leased from a communication service provider. There are two 4 × 8 (4 inputs and 8 outputs) switches in this network. For each switch, four output ports are folded into the input ports to allow communication between computers in the same office. Four other output ports allow communication between the two offices. Figure 8.5 shows the situation.

## Slide 255: Figure 8.5 Circuit-switched network used in Example 8.2

## Slide 256: Figure 8.6 Delay in a circuit-switched network

## Slide 257: Note
Switching at the physical layer in the traditional telephone network uses the circuit-switching approach.

## Slide 258: 8-2 DATAGRAM NETWORKS
In data communications, we need to send messages from one end system to another. If the message is going to pass through a packet-switched network, it needs to be divided into packets of fixed or variable size.. The size of the packet is determined by the network and the governing protocol.
Topics discussed in this section:
Routing Table Efficiency Delay
Datagram Networks in the Internet

## Slide 259: Note
In a packet-switched network, there is no resource reservation; resources are allocated on demand.

## Slide 260: Figure 8.7 A datagram network with four switches (routers)

## Slide 261: Figure 8.8 Routing table in a datagram network

## Slide 262: Note
A switch in a datagram network uses a routing table that is based on the destination address.

## Slide 263: Note
The destination address in the header of a packet in a datagram network
remains the same during the entire journey of the packet.

## Slide 264: Figure 8.9 Delay in a datagram network

## Slide 265: Note
Switching in the Internet is done by using the datagram approach
to packet switching at the network layer.

## Slide 266: 8-3 VIRTUAL-CIRCUIT NETWORKS
A virtual-circuit network is a cross between a circuit- switched network and a datagram network. It has some characteristics of both.
Topics discussed in this section:
Addressing Three Phases Efficiency Delay
Circuit-Switched Technology in WANs

## Slide 267: Figure 8.10 Virtual-circuit network

## Slide 268: Figure 8.11 Virtual-circuit identifier

## Slide 269: Figure 8.12 Switch and tables in a virtual-circuit network

## Slide 270: Figure 8.13 Source-to-destination data transfer in a virtual-circuit network

## Slide 271: Figure 8.14 Setup request in a virtual-circuit network

## Slide 272: Figure 8.15 Setup acknowledgment in a virtual-circuit network

## Slide 273: Note
In virtual-circuit switching, all packets belonging to the same source and destination travel the same path; but the packets may arrive at the
destination with different delays
if resource allocation is on demand.

## Slide 274: Figure 8.16 Delay in a virtual-circuit network

## Slide 275: Note
Switching at the data link layer in a switched WAN is normally implemented by using
virtual-circuit techniques.

## Slide 276: 8-4 STRUCTURE OF A SWITCH
We use switches in circuit-switched
and packet-
switched networks. In this section, we discuss the structures of the switches used in each type of network.
Topics discussed in this section: Structure of Circuit Switches Structure of Packet Switches

## Slide 277: Figure 8.17 Crossbar switch with three inputs and four outputs

## Slide 278: Figure 8.18 Multistage switch

## Slide 279: Note
In a three-stage switch, the total number of crosspoints is
2kN + k(N/n)2
which is much smaller than the number of
crosspoints in a single-stage switch (N2).

## Slide 280: Example 8.3
Design a three-stage, 200 × 200 switch (N = 200) with k = 4 and n = 20.
Solution
In the first stage we have N/n or 10 crossbars, each of size 20 × 4. In the second stage, we have 4 crossbars, each of size 10 × 10. In the third stage, we have 10 crossbars, each of size 4 × 20. The total number of crosspoints is 2kN + k(N/n)2, or 2000 crosspoints. This is 5 percent of the number of crosspoints in a single-stage switch (200 × 200 = 40,000).

## Slide 281: Note
According to the Clos criterion:
n = (N/2)1/2
k > 2n – 1
Crosspoints ≥ 4N [(2N)1/2 – 1]

## Slide 282: Example 8.4
Redesign the previous three-stage, 200 × 200 switch, using the Clos criteria with a minimum number of crosspoints.
Solution
We let n = (200/2)1/2, or n = 10. We calculate k = 2n − 1 =
19. In the first stage, we have 200/10, or 20, crossbars, each with 10 × 19 crosspoints. In the second stage, we have 19 crossbars, each with 10 × 10 crosspoints. In the third stage, we have 20 crossbars each with 19 × 10 crosspoints. The total number of crosspoints is 20(10 × 19) + 19(10 × 10) + 20(19 ×10) = 9500.

## Slide 283: Figure 8.19 Time-slot interchange

## Slide 284: Figure 8.20 Time-space-time switch

## Slide 285: Figure 8.21 Packet switch components

## Slide 286: Figure 8.22 Input port

## Slide 287: Figure 8.23 Output port

## Slide 288: Figure 8.24 A banyan switch

## Slide 289: Figure 8.25 Examples of routing in a banyan switch

## Slide 290: Figure 8.26 Batcher-banyan switch