## Slide 1
Data can be corrupted during transmission.
Some applications require that errors be detected and corrected.
10.1
In a single-bit error, only 1 bit in the data unit has changed.

## Slide 2: Figure 10.1 Single-bit error
10.2

## Slide 3: Figure 10.2 Burst error of length 8
10.3
A burst error means that 2 or more bits in the data unit have changed.

## Slide 4: Figure 10.3 The structure of encoder and decoder
10.4
To detect or correct errors, we need to send extra (redundant) bits with data.

## Slide 5: Figure 10.4 XORing of two single bits or two words
In modulo-N arithmetic, we use only the integers in the range 0 to N −1, inclusive.

## Slide 6: 10-2 BLOCK CODING
In block coding, we divide our message into blocks, each of k bits, called datawords.. We add r redundant bits to each block to make the length n = k + r.... The resulting n-bit blocks are called codewords..
Figure 10.5 Datawords and codewords in block coding

## Slide 7: Example 10.1
The 4B/5B block coding discussed in Chapter 4 is a good example of this type of coding. In this coding scheme, k = 4 and n = 5. As we saw, we have 2k = 16 datawords and 2n = 32 codewords. We saw that 16 out of 32 codewords are used for message transfer and the rest are either used for other purposes or unused.

## Slide 8: Figure 10.6 Process of error detection in block coding

## Slide 9: Example 10.2
Let us assume that k = 2 and n = 3. Table 10.1 shows the list of datawords and codewords. Later, we will see how to derive a codeword from a dataword.
Assume the sender encodes the dataword 01 as 011 and sends it to the receiver. Consider the following cases:
1. The receiver receives 011. It is a valid codeword. The receiver extracts the dataword 01 from it.
2. The codeword is corrupted during transmission, and 111 is received. This is not a valid codeword and is discarded.
The codeword is corrupted during transmission, and 000 is received. This is a valid codeword. The receiver incorrectly extracts the dataword 00. Two corrupted bits have made the error undetectable.

## Slide 10: Table 10.1 A code for error detection (Example 10.2)
An error-detecting code can detect only the types of errors for which it is designed; other types of errors may remain undetected.

## Slide 11: Figure 10.7 Structure of encoder and decoder in error correction

## Slide 12: Example 10.3
Let us add more redundant bits to Example 10.2 to see if the receiver can correct an error without knowing what was actually sent. We add 3 redundant bits to the 2-bit dataword to make 5-bit codewords. Table 10.2 shows the datawords and codewords. Assume the dataword is 01. The sender creates the codeword 01011. The codeword is corrupted during transmission, and 01001 is received. First, the receiver finds that the received codeword is not in the table. This means an error has occurred. The receiver, assuming that there is only 1 bit corrupted, uses the following strategy to guess the correct dataword.

## Slide 13: Example 10.3 (continued)
1.
Comparing the received codeword with the first
codeword in the table (01001 versus 00000), the receiver decides that the first codeword is not the one that was sent because there are two different bits.
By the same reasoning, the original codeword cannot be the third or fourth one in the table.
The original codeword must be the second one in the table because this is the only one that differs from the received codeword by 1 bit. The receiver replaces 01001 with 01011 and consults the table to find the dataword 01.

## Slide 14: Table 10.2 A code for error correction (Example 10.3)
The Hamming distance between two words is the number of differences between corresponding bits.

## Slide 15: Example 10.4
Let us find the Hamming distance between two pairs of words.
1. The Hamming distance d(000, 011) is 2 because
2. The Hamming distance d(10101, 11110) is 3 because
The minimum Hamming distance is the smallest Hamming distance between all possible pairs in a set of words.

## Slide 16: Example 10.5
Find the minimum Hamming distance of the coding scheme in Table 10.1.
Solution
We first find all Hamming distances.
The dmin in this case is 2.

## Slide 17: Example 10.6
Find the minimum Hamming distance of the coding scheme in Table 10.2.
Solution
We first find all the Hamming distances.
The dmin in this case is 3.
To guarantee the detection of up to s errors in all cases, the minimum Hamming distance in a block
code must be dmin = s + 1.

## Slide 18: Example 10.7
The minimum Hamming distance for our first code scheme (Table 10.1) is 2. This code guarantees detection of only a single error. For example, if the third codeword
(101) is sent and one error occurs, the received codeword does not match any valid codeword. If two errors occur, however, the received codeword may match a valid codeword and the errors are not detected.

## Slide 19: Example 10.8
Our second block code scheme (Table 10.2) has dmin = 3. This code can detect up to two errors. Again, we see that when any of the valid codewords is sent, two errors create a codeword which is not in the table of valid codewords. The receiver cannot be fooled.
However, some combinations of three errors change a valid codeword to another valid codeword. The receiver accepts the received codeword and the errors are undetected.

## Slide 20: Figure 10.8 Geometric concept for finding dmin in error detection

## Slide 21: Figure 10.9 Geometric concept for finding dmin in error correction
To guarantee correction of up to t errors in all cases, the minimum Hamming distance in a block code
must be dmin = 2t + 1.

## Slide 22: Example 10.9
A code scheme has a Hamming distance dmin = 4. What is the error detection and correction capability of this scheme?
Solution
This code guarantees the detection of up to three errors (s = 3), but it can correct up to one error In other words, if this code is used for error correction, part of its capability is wasted Error correction codes need to have an odd minimum distance (3, 5, 7, . . . ).
In a linear block code, the exclusive OR (XOR) of any two valid codewords creates another valid codeword.

## Slide 23: Example 10.10
Let us see if the two codes we defined in Table 10.1 and Table 10.2 belong to the class of linear block codes.
The scheme in Table 10.1 is a linear block code because the result of XORing any codeword with any other codeword is a valid codeword. For example, the XORing of the second and third codewords creates the fourth one.
The scheme in Table 10.2 is also a linear block code. We can create all four codewords by XORing two other codewords.

## Slide 24: Example 10.11
In our first code (Table 10.1), the numbers of 1s in the nonzero codewords are 2, 2, and 2. So the minimum Hamming distance is dmin = 2. In our second code (Table 10.2), the numbers of 1s in the nonzero codewords are 3, 3, and 4. So in this code we have dmin = 3.
A simple parity-check code is a single-bit error-detecting code in which
n = k + 1 with dmin = 2.

## Slide 25: Table 10.3 Simple parity-check code C(5, 4)

## Slide 26: Figure 10.10 Encoder and decoder for simple parity-check code

## Slide 27: Example 10.12
Let us look at some transmission scenarios. Assume the sender sends the dataword 1011. The codeword created from this dataword is 10111, which is sent to the receiver. We examine five cases:
No error occurs; the received codeword is 10111. The syndrome is 0. The dataword 1011 is created.
One single-bit error changes a1 . The received codeword is 10011. The syndrome is 1. No dataword is created.
One single-bit error changes r0 . The received codeword is 10110. The syndrome is 1. No dataword is created.

## Slide 28: Example 10.12 (continued)
An error changes r0 and a second error changes a3 . The received codeword is 00110. The syndrome is 0. The dataword 0011 is created at the receiver. Note that here the dataword is wrongly created due to the syndrome value.
Three bits—a3, a2, and a1—are changed by errors. The received codeword is 01011. The syndrome is 1.
The dataword is not created. This shows that the simple parity check, guaranteed to detect one single error, can also find any odd number of errors.

## Slide 29
A simple parity-check code can detect an odd number of errors.
All Hamming codes discussed in this book have dmin = 3.
The relationship between m and n in these codes is n = 2m − 1.

## Slide 30: Figure 10.11 Two-dimensional parity-check code

## Slide 31: Figure 10.11 Two-dimensional parity-check code

## Slide 32: Figure 10.11 Two-dimensional parity-check code

## Slide 33: Table 10.4 Hamming code C(7, 4)

## Slide 34: Figure 10.12 The structure of the encoder and decoder for a Hamming code

## Slide 35: Table 10.5 Logical decision made by the correction logic analyzer

## Slide 36: Example 10.13
Let us trace the path of three datawords from the sender to the destination:
The dataword 0100 becomes the codeword 0100011. The codeword 0100011 is received. The syndrome is 000, the final dataword is 0100.
The dataword 0111 becomes the codeword 0111001. The syndrome is 011. After flipping b2 (changing the 1 to 0), the final dataword is 0111.
The dataword 1101 becomes the codeword 1101000. The syndrome is 101. After flipping b0, we get 0000, the wrong dataword. This shows that our code cannot correct two errors.

## Slide 37: Example 10.14
We need a dataword of at least 7 bits. Calculate values of k and n that satisfy this requirement.
Solution
We need to make k = n − m greater than or equal to 7, or 2m − 1 − m ≥ 7.
If we set m = 3, the result is n = 23 − 1 and k = 7 − 3, or 4, which is not acceptable.
If we set m = 4, then n = 24 − 1 = 15 and k = 15 − 4 = 11, which satisfies the condition. So the code is
C(15, 11)

## Slide 38: Figure 10.13 Burst error correction using Hamming code

## Slide 39: 10-4 CYCLIC CODES
Cyclic codes are special linear block codes with one extra property. In a cyclic code, if a codeword is cyclically shifted (rotated), the result is another codeword.
Topics discussed in this section: Cyclic Redundancy Check Hardware Implementation Polynomials
Cyclic Code Analysis Advantages of Cyclic Codes Other Cyclic Codes

## Slide 40: Table 10.6 A CRC code with C(7, 4)

## Slide 41: Figure 10.14 CRC encoder and decoder

## Slide 42: Figure 10.15 Division in CRC encoder

## Slide 43: Figure 10.16 Division in the CRC decoder for two cases

## Slide 44: Figure 10.17 Hardwired design of the divisor in CRC

## Slide 45: Figure 10.18 Simulation of division in CRC encoder

## Slide 46: Figure 10.19 The CRC encoder design using shift registers

## Slide 47: Figure 10.20 General design of encoder and decoder of a CRC code

## Slide 48: A polynomial to represent a binary word
Figure 10.21

## Slide 49: Figure 10.22 CRC division using polynomials

## Slide 50
In a cyclic code,
If s(x) ≠ 0, one or more bits is corrupted.
If s(x) = 0, either
No bit is corrupted. or
Some bits are corrupted, but the decoder failed to detect them.
The divisor in a cyclic code is normally called the generator polynomial
or simply the generator.

## Slide 51
In a cyclic code, those e(x) errors that are divisible by g(x) are not caught.
If the generator has more than one term and the coefficient of x0 is 1,
all single errors can be caught.

## Slide 52: Example 10.15
Which of the following g(x) values guarantees that a single-bit error is caught? For each case, what is the error that cannot be caught?
a. x + 1 b. x3 c. 1
Solution
No xi can be divisible by x + 1. Any single-bit error can be caught.
If i is equal to or greater than 3, xi is divisible by g(x). All single-bit errors in positions 1 to 3 are caught.
All values of i make xi divisible by g(x). No single-bit error can be caught. This g(x) is useless.

## Slide 53: Figure 10.23 Representation of two isolated single-bit errors using polynomials
If a generator cannot divide xt + 1 (t between 0 and n – 1),
then all isolated double errors can be detected.

## Slide 54: Example 10.16
Find the status of the following generators related to two isolated, single-bit errors.
a. x + 1 b. x4 + 1 c. x7 + x6 + 1 d. x15 + x14 + 1 Solution
This is a very poor choice for a generator. Any two errors next to each other cannot be detected.
This generator cannot detect two errors that are four positions apart.
This is a good choice for this purpose.
This polynomial cannot divide xt + 1 if t is less than 32,768. A codeword with two isolated errors up to 32,768 bits apart can be detected by this generator.

## Slide 55
A generator that contains a factor of x + 1 can detect all odd-numbered errors.
❏ All burst errors with L ≤ r will be detected.
❏ All burst errors with L = r + 1 will be detected with probability 1 – (1/2)r–1.
❏ All burst errors with L > r + 1 will be detected with probability 1 – (1/2)r.

## Slide 56: Example 10.17
Find the suitability of the following generators in relation to burst errors of different lengths.
a. x6 + 1 b. x18 + x7 + x + 1 c. x32 + x23 + x7 + 1
Solution
a. This generator can detect all burst errors with a length less than or equal to 6 bits; 3 out of 100 burst errors with length 7 will slip by; 16 out of 1000 burst errors of length 8 or more will slip by.

## Slide 57: Example 10.17 (continued)
b. This generator can detect all burst errors with a length less than or equal to 18 bits; 8 out of 1 million burst errors with length 19 will slip by; 4 out of 1 million burst errors of length 20 or more will slip by.
c. This generator can detect all burst errors with a length less than or equal to 32 bits; 5 out of 10 billion burst errors with length 33 will slip by; 3 out of 10 billion burst errors of length 34 or more will slip by.

## Slide 58: Note
A good polynomial generator needs to have the following characteristics:
It should have at least two terms.
The coefficient of the term x0 should be 1.
It should not divide xt + 1, for t
between 2 and n − 1.
It should have the factor x + 1.

## Slide 59: Table 10.7 Standard polynomials

## Slide 60: 10-5 CHECKSUM
The last error detection method we discuss here is called the checksum. The checksum is used in the Internet by several protocols although not at the data link layer. However, we briefly discuss it here to complete our discussion on error checking
Topics discussed in this section:
Idea
One’s Complement Internet Checksum

## Slide 61: Example 10.18
Suppose our data is a list of five 4-bit numbers that we want to send to a destination. In addition to sending these numbers, we send the sum of the numbers. For example, if the set of numbers is (7, 11, 12, 0, 6), we send (7, 11, 12,
0, 6, 36), where 36 is the sum of the original numbers. The receiver adds the five numbers and compares the result with the sum. If the two are the same, the receiver assumes no error, accepts the five numbers, and discards the sum. Otherwise, there is an error somewhere and the data are not accepted.

## Slide 62: Example 10.19
We can make the job of the receiver easier if we send the negative (complement) of the sum, called the checksum. In this case, we send (7, 11, 12, 0, 6, −36). The receiver
checksum).
can add all the numbers received (including the If the result is
0, it assumes no error;
otherwise, there is an error.
How can we represent the number 21 in one’s complement arithmetic using only four bits?
Solution
The number 21 in binary is 10101 (it needs five bits). We can wrap the leftmost bit and add it to the four rightmost bits. We have (0101 + 1) = 0110 or 6.

## Slide 63: Example 10.21
How can we represent the number −6
in one’s
complement arithmetic using only four bits?
Solution
In one’s complement arithmetic, the negative or complement of a number is found by inverting all bits Positive 6 is 0110; negative 6 is 1001. If we consider only
unsigned numbers, this is 9 In
other words, the complement of 6 is 9. Another way to find the
complement of a number in one’s complement arithmetic is to subtract the number from 2n − 1 (16 − 1 in this case).

## Slide 64: Example 10.22
Let us redo Exercise 10.19 using one’s complement arithmetic Figure 10 24 shows the process at the sender and at the receiver. The sender initializes the checksum to 0 and adds all data items and the checksum (the checksum is considered as one data item and is shown in color) The result is 36 However, 36 cannot be expressed in 4 bits. The extra two bits are wrapped and added with the sum to create the wrapped sum value 6 In the figure, we have shown the details in binary. The sum is then complemented, resulting in the checksum value 9 (15 − 6
= 9). The sender now sends six data items to the receiver including the checksum 9

## Slide 65: Example 10.22 (continued)
The receiver follows the same procedure as the sender. It adds all data items (including the checksum); the result is 45. The sum is wrapped and becomes 15. The wrapped sum is complemented and becomes 0. Since the value of the checksum is 0, this means that the data is not corrupted. The receiver drops the checksum and keeps the other data items. If the checksum is not zero, the entire packet is dropped.

## Slide 66: Figure 10.24 Example 10.22

## Slide 67: Note
Sender site:
The message is divided into 16-bit words.
The value of the checksum word is set to 0.
All words including the checksum are added using one’s complement addition.
The sum is complemented and becomes the checksum.
The checksum is sent with the data.

## Slide 68: Note
Receiver site:
The message (including checksum) is divided into 16-bit words.
All words are added using one’s complement addition.
The sum is complemented and becomes the new checksum.
If the value of checksum is 0, the message is accepted; otherwise, it is rejected.

## Slide 69: Example 10.23
Let us calculate the checksum for a text of 8 characters (“Forouzan”). The text needs to be divided into 2-byte (16-bit) words. We use ASCII (see Appendix A) to change each byte to a 2-digit hexadecimal number. For example, F is represented as 0x46 and o is represented as 0x6F. Figure 10.25 shows how the checksum is calculated at the sender and receiver sites. In part a of the figure, the value of partial sum for the first column is 0x36. We keep the rightmost digit (6) and insert the leftmost digit (3) as the carry in the second column. The process is repeated for each column. Note that if there is any corruption, the checksum recalculated by the receiver is not all 0s. We leave this an exercise.

## Slide 70: Figure 10.25 Example 10.23