## Slide 1: Chapter 11 Data Link Control
11.1
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2: 11-1 FRAMING
The data link layer needs to pack bits into frames,, so that each frame is distinguishable from another.... Our postal system practices a type of framing. The simple act of inserting a letter into an envelope separates one piece of information from another; the envelope serves as the delimiter..
Topics discussed in this section:
Fixed-Size Framing Variable-Size Framing
11.2

## Slide 3: Figure 11.1 A frame in a character-oriented protocol
11.2

## Slide 4: Figure 11.2 Byte stuffing and unstuffing
11.2

## Slide 5: Note
Byte stuffing is the process of adding 1 extra byte whenever there is a flag or escape character in the text.
11.2

## Slide 6: Figure 11.3 A frame in a bit-oriented protocol
11.2

## Slide 7: Note
Bit stuffing is the process of adding one extra 0 whenever five consecutive 1s follow a 0 in the data, so that the receiver does not mistake
the pattern 0111110 for a flag.
11.2

## Slide 8: Figure 11.4 Bit stuffing and unstuffing
11.2

## Slide 9: 11-2 FLOW AND ERROR CONTROL
The most important responsibilities of the data link layer are flow control and error control. Collectively, these functions are known as data link control..
11.2
Topics discussed in this section:
Flow Control Error Control

## Slide 10: Note
Flow control refers to a set of procedures used to restrict the amount of data
that the sender can send before waiting for acknowledgment.

## Slide 11: Note
Error control in the data link layer is based on automatic repeat request, which is the retransmission of data.

## Slide 12: 11-3 PROTOCOLS
Now let us see how the data link layer can combine framing, flow control, and error control to achieve the delivery of data from one node to another.. The protocols are normally implemented in software by using one of the common programming languages.. To make our discussions language-free, we have written in pseudocode a version of each protocol that concentrates mostly on the procedure instead of delving into the details of language rules..

## Slide 13: Figure 11.5 Taxonomy of protocols discussed in this chapter

## Slide 14: 11-4 NOISELESS CHANNELS
Let us first assume we have an ideal channel in which no frames are lost, duplicated, or corrupted. We introduce two protocols for this type of channel..
Topics discussed in this section:
Simplest Protocol
Stop-and-Wait Protocol

## Slide 15: Figure 11.6 The design of the simplest protocol with no flow or error control

## Slide 16: Algorithm 11.1 Sender-site algorithm for the simplest protocol

## Slide 17: Algorithm 11.2 Receiver-site algorithm for the simplest protocol

## Slide 18: Example 11.1
Figure 11.7 shows an example of communication using this protocol. It is very simple. The sender sends a sequence of frames without even thinking about the receiver. To send three frames, three events occur at the sender site and three events at the receiver site. Note that the data frames are shown by tilted boxes; the height of the box defines the transmission time difference between the first bit and the last bit in the frame.

## Slide 19: Figure 11.7 Flow diagram for Example 11.1

## Slide 20: Figure 11.8 Design of Stop-and-Wait Protocol

## Slide 21: Algorithm 11.3 Sender-site algorithm for Stop-and-Wait Protocol

## Slide 22: Algorithm 11.4 Receiver-site algorithm for Stop-and-Wait Protocol

## Slide 23: Example 11.2
Figure 11.9 shows an example of communication using this protocol. It is still very simple. The sender sends one frame and waits for feedback from the receiver. When the ACK arrives, the sender sends the next frame. Note that sending two frames in the protocol involves the sender in four events and the receiver in two events.

## Slide 24: Figure 11.9 Flow diagram for Example 11.2

## Slide 25: 11-5 NOISY CHANNELS
Although the Stop-and-Wait Protocol gives us an idea of how to add flow control to its predecessor, noiseless channels are nonexistent.. We discuss three protocols in this section that use error control.
Topics discussed in this section:
Stop-and-Wait Automatic Repeat Request Go-Back-N Automatic Repeat Request Selective Repeat Automatic Repeat Request

## Slide 26: Note
Error correction in Stop-and-Wait ARQ is done by keeping a copy of the sent frame and retransmitting of the frame when the timer expires.

## Slide 27: Note
In Stop-and-Wait ARQ, we use sequence numbers to number the frames.
The sequence numbers are based on modulo-2 arithmetic.

## Slide 28: Note
In Stop-and-Wait ARQ, the acknowledgment number always announces in modulo-2 arithmetic the sequence number of the next frame expected.

## Slide 29: Figure 11.10 Design of the Stop-and-Wait ARQ Protocol

## Slide 30
Algorithm 11.5 Sender-site algorithm for Stop-and-Wait ARQ
(continued)

## Slide 31: (continued)
Algorithm 11.5 Sender-site algorithm for Stop-and-Wait ARQ

## Slide 32: Algorithm 11.6 Receiver-site algorithm for Stop-and-Wait ARQ Protocol

## Slide 33: Example 11.3
Figure 11.11 shows an example of Stop-and-Wait ARQ. Frame 0 is sent and acknowledged. Frame 1 is lost and resent after the time-out. The resent frame 1 is acknowledged and the timer stops. Frame 0 is sent and acknowledged, but the acknowledgment is lost. The sender has no idea if the frame or the acknowledgment is lost, so after the time-out, it resends frame 0, which is acknowledged.

## Slide 34: Figure 11.11 Flow diagram for Example 11.3

## Slide 35: Example 11.4
Assume that, in a Stop-and-Wait ARQ system, the bandwidth of the line is 1 Mbps, and 1 bit takes 20 ms to make a round trip. What is the bandwidth-delay product? If the system data frames are 1000 bits in length, what is the utilization percentage of the link?
Solution
The bandwidth-delay product is

## Slide 36: Example 11.4 (continued)
The system can send 20,000 bits during the time it takes for the data to go from the sender to the receiver and then back again. However, the system sends only 1000 bits. We can say that the link utilization is only 1000/20,000, or 5 percent. For this reason, for a link with a high bandwidth or long delay, the use of Stop-and-Wait ARQ wastes the capacity of the link.

## Slide 37: Example 11.5
What is the utilization percentage of the link in Example 11 4 if we have a protocol that can send up to
15 frames before stopping and worrying about the acknowledgments?
Solution
The bandwidth-delay product is still 20,000 bits. The system can send up to 15 frames or 15,000 bits during a round trip. This means the utilization is 15,000/20,000, or 75 percent. Of course, if there are damaged frames, the utilization percentage is much less because frames have to be resent.

## Slide 38: Note
In the Go-Back-N Protocol, the sequence numbers are modulo 2m,
where m is the size of the sequence number field in bits.

## Slide 39: Figure 11.12 Send window for Go-Back-N ARQ

## Slide 40: Note
The send window is an abstract concept defining an imaginary box of size 2m − 1 with three variables: Sf, Sn, and Ssize.

## Slide 41: Note
The send window can slide one or more slots when a valid acknowledgment arrives.

## Slide 42: Figure 11.13 Receive window for Go-Back-N ARQ

## Slide 43: Note
The receive window is an abstract concept defining an imaginary box of size 1 with one single variable Rn.
The window slides
when a correct frame has arrived; sliding occurs one slot at a time.

## Slide 44: Figure 11.14 Design of Go-Back-N ARQ

## Slide 45: Figure 11.15 Window size for Go-Back-N ARQ

## Slide 46: Note
In Go-Back-N ARQ, the size of the send window must be less than 2m;
the size of the receiver window is always 1.

## Slide 47
Algorithm 11.7 Go-Back-N sender algorithm
(continued)

## Slide 48: Algorithm 11.7 Go-Back-N sender algorithm
(continued)

## Slide 49: Algorithm 11.8 Go-Back-N receiver algorithm

## Slide 50: Example 11.6
Figure 11.16 shows an example of Go-Back-N. This is an example of a case where the forward channel is reliable, but the reverse is not. No data frames are lost, but some ACKs are delayed and one is lost. The example also shows how cumulative acknowledgments can help if acknowledgments are delayed or lost. After initialization, there are seven sender events. Request events are triggered by data from the network layer; arrival events are triggered by acknowledgments from the physical layer. There is no time-out event here because all outstanding frames are acknowledged before the timer expires. Note that although ACK 2 is lost, ACK 3 serves as both ACK 2 and ACK 3.

## Slide 51: Figure 11.16 Flow diagram for Example 11.6

## Slide 52: Example 11.7
Figure 11.17 shows what happens when a frame is lost. Frames 0, 1, 2, and 3 are sent However, frame 1 is lost The receiver receives frames 2 and 3, but they are discarded because they are received out of order The sender receives no acknowledgment about frames 1, 2, or
3 Its timer finally expires The sender sends all outstanding frames (1, 2, and 3) because it does not know what is wrong Note that the resending of frames 1, 2, and 3 is the response to one single event. When the sender is responding to this event, it cannot accept the triggering of other events. This means that when ACK 2 arrives, the sender is still busy with sending frame 3

## Slide 53: Example 11.7 (continued)
The physical layer must wait until this event is completed and the data link layer goes back to its sleeping state. We have shown a vertical line to indicate the delay. It is the same story with ACK 3; but when ACK 3 arrives, the sender is busy responding to ACK 2. It happens again when ACK 4 arrives. Note that before the second timer expires, all outstanding frames have been sent and the timer is stopped.

## Slide 54: Figure 11.17 Flow diagram for Example 11.7

## Slide 55: Note
Stop-and-Wait ARQ is a special case of Go-Back-N ARQ in which the size of the send window is 1.

## Slide 56: Figure 11.18 Send window for Selective Repeat ARQ

## Slide 57: Figure 11.19 Receive window for Selective Repeat ARQ

## Slide 58: Figure 11.20 Design of Selective Repeat ARQ

## Slide 59: Figure 11.21 Selective Repeat ARQ, window size

## Slide 60: Note
In Selective Repeat ARQ, the size of the sender and receiver window
must be at most one-half of 2m.

## Slide 61
Algorithm 11.9 Sender-site Selective Repeat algorithm
(continued)

## Slide 62
Algorithm 11.9 Sender-site Selective Repeat algorithm
(continued)
11.62
(continued)

## Slide 63: Algorithm 11.9 Sender-site Selective Repeat algorithm
(continued)

## Slide 64: Algorithm 11.10 Receiver-site Selective Repeat algorithm

## Slide 65: Algorithm 11.10 Receiver-site Selective Repeat algorithm

## Slide 66: Figure 11.22 Delivery of data in Selective Repeat ARQ

## Slide 67: Example 11.8
This example is similar to Example 11.3 in which frame 1 is lost. We show how Selective Repeat behaves in this case. Figure 11.23 shows the situation. One main difference is the number of timers. Here, each frame sent or resent needs a timer, which means that the timers need to be numbered (0, 1, 2, and 3). The timer for frame 0 starts at the first request, but stops when the ACK for this frame arrives. The timer for frame 1 starts at the second request, restarts when a NAK arrives, and finally stops when the last ACK arrives. The other two timers start when the corresponding frames are sent and stop at the last arrival event.

## Slide 68: Example 11.8 (continued)
At the receiver site we need to distinguish between the acceptance of a frame and its delivery to the network layer. At the second arrival, frame 2 arrives and is stored and marked, but it cannot be delivered because frame 1 is missing. At the next arrival, frame 3 arrives and is marked and stored, but still none of the frames can be delivered. Only at the last arrival, when finally a copy of frame 1 arrives, can frames 1, 2, and 3 be delivered to the network layer. There are two conditions for the delivery of frames to the network layer: First, a set of consecutive frames must have arrived. Second, the set starts from the beginning of the window.

## Slide 69: Example 11.8 (continued)
Another important point is that a NAK is sent after the second arrival, but not after the third, although both situations look the same. The reason is that the protocol does not want to crowd the network with unnecessary NAKs and unnecessary resent frames. The second NAK would still be NAK1 to inform the sender to resend frame 1 again; this has already been done. The first NAK sent is remembered (using the nakSent variable) and is not sent again until the frame slides. A NAK is sent once for each window position and defines the first slot in the window.

## Slide 70: Example 11.8 (continued)
The next point is about the ACKs. Notice that only two ACKs are sent here. The first one acknowledges only the first frame; the second one acknowledges three frames. In Selective Repeat, ACKs are sent when data are delivered to the network layer. If the data belonging to n frames are delivered in one shot, only one ACK is sent for all of them.

## Slide 71: Figure 11.23 Flow diagram for Example 11.8

## Slide 72: Figure 11.24 Design of piggybacking in Go-Back-N ARQ

## Slide 73: 11-6 HDLC
High-level Data Link Control (HDLC) is a bit-oriented protocol for communication over point-to-point and multipoint links.. It implements the ARQ mechanisms we discussed in this chapter.
Topics discussed in this section: Configurations and Transfer Modes Frames
Control Field

## Slide 74: Figure 11.25 Normal response mode

## Slide 75: Figure 11.26 Asynchronous balanced mode

## Slide 76: Figure 11.27 HDLC frames

## Slide 77: Figure 11.28 Control field format for the different frame types

## Slide 78: Table 11.1 U-frame control command and response

## Slide 79: Example 11.9
Figure 11.29 shows how U-frames can be used for connection establishment and connection release. Node A asks for a connection with a set asynchronous balanced mode (SABM) frame; node B gives a positive response with an unnumbered acknowledgment (UA) frame. After these two exchanges, data can be transferred between the two nodes (not shown in the figure). After data transfer, node A sends a DISC (disconnect) frame to release the connection; it is confirmed by node B responding with a UA (unnumbered acknowledgment).

## Slide 80: Figure 11.29 Example of connection and disconnection

## Slide 81: Example 11.10
Figure 11.30 shows an exchange using piggybacking. Node A begins the exchange of information with an I-frame numbered 0 followed by another I-frame numbered 1. Node B piggybacks its acknowledgment of both frames onto an I-frame of its own. Node B’s first I-frame is also numbered 0 [N(S) field] and contains a 2 in its N(R) field, acknowledging the receipt of A’s frames 1 and 0 and indicating that it expects frame 2 to arrive next. Node B transmits its second and third I-frames (numbered 1 and 2) before accepting further frames from node A.

## Slide 82: Example 11.10 (continued)
Its N(R) information, therefore, has not changed: B frames 1 and 2 indicate that node B is still expecting A’s frame 2 to arrive next. Node A has sent all its data. Therefore, it cannot piggyback an acknowledgment onto an I-frame and sends an S-frame instead. The RR code indicates that A is still ready to receive. The number 3 in the N(R) field tells B that frames 0, 1, and 2 have all been accepted and that A is now expecting frame number 3.

## Slide 83: Figure 11.30 Example of piggybacking without error

## Slide 84: Example 11.11
Figure 11.31 shows an exchange in which a frame is lost. Node B sends three data frames (0, 1, and 2), but frame 1 is lost. When node A receives frame 2, it discards it and sends a REJ frame for frame 1. Note that the protocol being used is Go-Back-N with the special use of an REJ frame as a NAK frame. The NAK frame does two things here: It confirms the receipt of frame 0 and declares that frame 1 and any following frames must be resent. Node B, after receiving the REJ frame, resends frames 1 and 2. Node A acknowledges the receipt by sending an RR frame (ACK) with acknowledgment number 3.

## Slide 85: Figure 11.31 Example of piggybacking with error

## Slide 86: 11-7 POINT-TO-POINT PROTOCOL
Although HDLC is a general protocol that can be used for both point-to-point and multipoint configurations, one of the most common protocols for point-to-point access is the Point-to-Point Protocol (PPP). PPP is a byte-oriented protocol..
Topics discussed in this section:
Framing Transition Phases Multiplexing Multilink PPP

## Slide 87: Figure 11.32 PPP frame format

## Slide 88: Note
PPP is a byte-oriented protocol using byte stuffing with the escape byte 01111101.

## Slide 89: Figure 11.33 Transition phases

## Slide 90: Figure 11.34 Multiplexing in PPP

## Slide 91: Figure 11.35 LCP packet encapsulated in a frame

## Slide 92: Table 11.2 LCP packets

## Slide 93: Table 11.3 Common options

## Slide 94: Figure 11.36 PAP packets encapsulated in a PPP frame

## Slide 95: Figure 11.37 CHAP packets encapsulated in a PPP frame

## Slide 96: Figure 11.38 IPCP packet encapsulated in PPP frame

## Slide 97: Table 11.4 Code value for IPCP packets

## Slide 98: Figure 11.39 IP datagram encapsulated in a PPP frame

## Slide 99: Figure 11.40 Multilink PPP

## Slide 100: Example 11.12
Let us go through the phases followed by a network layer packet as it is transmitted through a PPP connection. Figure 11.41 shows the steps. For simplicity, we assume unidirectional movement of data from the user site to the system site (such as sending an e-mail through an ISP).
The first two frames show link establishment. We have chosen two options (not shown in the figure): using PAP for authentication and suppressing the address control fields. Frames 3 and 4 are for authentication. Frames 5 and 6 establish the network layer connection using IPCP.
11.100

## Slide 101: Example 11.12 (continued)
The next several frames show that some IP packets are encapsulated in the PPP frame. The system (receiver) may have been running several network layer protocols, but it knows that the incoming data must be delivered to the IP protocol because the NCP protocol used before the data transfer was IPCP.
After data transfer, the user then terminates the data link connection, which is acknowledged by the system. Of course the user or the system could have chosen to terminate the network layer IPCP and keep the data link layer running if it wanted to run another NCP protocol.
11.100

## Slide 102: Figure 11.41 An example
11.100

## Slide 103: Figure 11.41 An example (continued)
11.100